## Slide 1: Farm Warehouse Management

## Slide 2: Aim
To build a smart IOT based system that helps monitor activity inside the warehouse.
Monitoring the stocks inside the warehouse helps avoid any damage that could happen as result of fire or rodents infiltration.

## Slide 3: Smart Warehouse Features
Pest Detection
Fire Detection
Warehouse break in detection

## Slide 4: Implementation
Components:
Hardware
  Raspberry pi
  Ultrasonic sensor
  LDR sensor
Software
  Python – Django, tensorflow

## Slide 5: Implementation
The sensors that are located at the warehouse gets triggered by any change in the surroundings.
This triggers is communicated to the raspberry pi module which turn the camera stored in the warehouse on.
The video recorded by the camera is sent to raspberry pi module which analysis the video frame by frame using a pre-trained machine learning model.
The machine learning model help detect the presence of rodents, fire or any human presence in the warehouse.

## Slide 6: About the ML model
The model is Convolutional Neural Network that helps classifying the images.
The model is trained on a dataset that has 1795 images
The model does predict the presence of rodents, fire and human but also has a lot of drawbacks.
The drawbacks can be improved by using a pre-trained model like vgg16, vgg19 or resnet.
Making use of transfer learning and a large dataset can make the predictions more accurate and faster.

## Slide 7: About the hardware
Hardware consists of the various sensor for running the model.
If either one of the sensor is triggered, the ML model is run after catching the photo via the RPi camera system.
As of now, temperature sensor, humidity sensor and fan control is being simulated along with the camera system.
Given the hardware, driver codes can be developed and their respective triggers can be set for activating the model.

## Slide 8: Further improvements
More pests can be added to the classification model and their images trained.
More sensors and additional cloud capabilities are also possible to be fitted since there are a lot of GPIO pins available.
Face recognition can be implemented for security purposes not included here due to time constraints.
App can be created for accessing the web server to reduce complexity.

## Slide 9: Sample cost for different warehouses
Small warehouse (about 10mx10m):
  Raspberry Pi Zero W = 1730
  2 X LDR Module =2*49 = 98
  2 X Ultrasonic =2*75 = 150
  1 X DHT-11 (temp and humidity) = 82.50
  Camera = 290
  Ai thinker ESP82 with CAM = 695
  TOTAL = 3046

## Slide 10: Continued…
Medium Warehouse (about 50mx50m)
  Raspberry Pi Zero W = 1730
  4 X LDR Module = 4 * 49 = 196
  4 X Ultrasonic sensor = 4 * 75 = 300
  2 X DHT-11(Temp and humidity sensor) = 2 * 82.50 = 165
  Camera = 290
  3 X Ai thinker ESP82 with CAM = 3 * 695 = 2085
  TOTAL = 4766

## Slide 11
Note that all the prices mentioned are retail rates , if ordered in a bulk they get cheaper.
The components mentioned are for an ideal case scenario, the user can reduce the components as desired to meet their warehouse requirements.